## Slide 1
Development of Mapping and Navigation for
Autonomous Aerial Vehicle
Name : Ryan Seah Meng Yong
Admission No.: 103910D
Diploma : Aerospace Systems and Management
Project Supervisor: Mr. Goh Pit Kiam

## Slide 2
History
The Challenge
The Map
PID Tuning
OVERVIEW

## Slide 3: HISTORY
In 2011, we navigated through course using a given color track
In 2012, we had to develop and navigate through the course using a 60 markers track

## Slide 4
THE CHALLENGE
A limitation of 20 markers with the size of 20 cm (L) x 20 cm (W) x 5 cm (H).
A course that is 14 m (L) x 17 m (W).

## Slide 5: THE SOLUTION
We develop a scaled map .
Together with the use of Iterative Closest Point (ICP).
To calculate the accurate position and heading of the craft

## Slide 6: THE MAP
Actual
On Program
1 : 1
Internal representation

## Slide 7: WHAT IS ICP?
It aligns a set of scanned 2D or 3D data with a set of known 2D or 3D data.
Rotate
Translate
Pre-Known Points
Scanned Points

## Slide 8: THE ICP
Perceived position
Actual position
Pre-Known Points
Scanned Points
It can be also use to locate the position and heading of the aircraft

## Slide 9: THE ICP
The rough gauge of the current position & heading of the aircraft.
A set of scanned point
A known set of pre-known points.
In return, it gives us a translation and rotation matrix
Position, Heading,
Pre-Known Points & Scan Points

## Slide 10: THE ICP
Position : Optical flow.
Heading : On board Gyro

## Slide 11: THE POINTS
Every 10 cm, 1 point

## Slide 12: THE SCANNERS
Scanner |  | 
Number of points | 680 | 320
Range/m | 5 | 7

## Slide 13
THE ROTATION
Heading!
cos Ө
-sin Ө
sin Ө
cos Ө
=
R

## Slide 14: THE TRANSLATION
Position!
x
y
=
Translation ( x )

## Slide 15: THE REFLECTION
xx = 3.53 yy = 12.73
icpx = 3.51 icpy = 12.71
deg = 0.00 icpdeg = 0.00
R:
1.00 -0.00
0.00 1.00
xx = 3.53 yy = 12.73
icpx = 11.74 icpy = 4.54
deg = 0.00 icpdeg = 90.00
R:
0.00 1.00
1.00 -0.00

## Slide 16: THE REFLECTION
Reflect
Rotate
Translate
Pre-Known Points
Scanned Points

## Slide 17: THE REFLECTION
cos 2A
sin 2A
sin 2A
-cos 2A
=
Reflection
A reflection matrix has a determinant of -1.

## Slide 18: THE REFLECTION
cos 2A
sin 2A
sin 2A
-cos 2A
=
Ref.
cos Ө
-sin Ө
sin Ө
cos Ө
=
Rot.
Actual ICP Rotation = reflection x rotation
cos Ө
-sin Ө
sin Ө
cos Ө
=
R
cos 2A
sin 2A
sin 2A
-cos 2A

## Slide 19: THE REFLECTION
cos Ө
sin Ө
-sin Ө
cos Ө
=
R
cos 2A
sin 2A
sin 2A
-cos 2A
=
cos 2A cos Ө - sin 2A sin Ө
sin 2A cos Ө + cos 2A sin Ө
cos 2A sin Ө + sin 2A cos Ө
sin 2A sin Ө - cos 2A cos Ө
=
cos( 2A + Ө)
sin( 2A + Ө)
-cos( 2A + Ө)
sin( 2A + Ө)
Clockwise Matrix

## Slide 20: THE REFLECTION
cos Ө
-sin Ө
sin Ө
cos Ө
=
R
cos 2A
sin 2A
sin 2A
-cos 2A
=
cos 2A cos Ө + sin 2A sin Ө
sin 2A cos Ө – cos 2A sin Ө
-cos 2A sin Ө + sin 2A cos Ө
-sin 2A sin Ө – cos 2A cos Ө
=
cos( 2A - Ө)
sin( 2A - Ө)
-cos( 2A - Ө)
sin( 2A - Ө)
Anti-Clockwise Matrix

## Slide 21: THE REFLECTION
R
=
cos( 2A + Ө)
sin( 2A + Ө)
-cos( 2A + Ө)
sin( 2A + Ө)
cos( 2A - Ө)
sin( 2A - Ө)
-cos( 2A - Ө)
sin( 2A - Ө)
OR
Since we know A is related to the points angle
Hence, A = 45ᵒ, 90ᵒ, 135ᵒ, 180ᵒ, 225ᵒ, 270ᵒ,315ᵒ and 360ᵒ
And u find the angle closest to the current angle.

## Slide 22: THE REFLECTION
R
=
cos( 2A + Ө)
sin( 2A + Ө)
-cos( 2A + Ө)
sin( 2A + Ө)
cos( 2A - Ө)
sin( 2A - Ө)
-cos( 2A - Ө)
sin( 2A - Ө)
OR
To speed up the processing, I’ve used the comparison of values to determine whether to use the clockwise matrix or anti clockwise matrix:
2A – Ө < 2A
2A + Ө > 2A

## Slide 23: THE REFLECTION
Heading from reflection!
xx = 3.40 yy = 13.60
icpx = 3.40 icpy = 13.60
deg = 0.00 icpdeg = 0.00
R:
1.00 -0.00
0.00 1.00
xx = 3.40 yy = 13.60
icpx = 12.57 icpy = 4.37
deg = 0.00 icpdeg = 0.00
R:
0.00 1.00
1.00 -0.00

## Slide 24
THE REFLECTION
P(x)
P(y)
cos Ө
-sin Ө
sin Ө
cos Ө
=
x1
y1
T(x)
T(y)
+
P(x)
P(y)
a
b
c
d
=
x1
y1
T’(x)
T’(y)
+
Matched points = reflection x scanned points + translation
Since, Matched points = scanned points

## Slide 25
T(x)
T(y)
=
x1 ( a – cos Ө ) + y1 ( b + sin Ө ) + T’( x )
x1 ( c + sin Ө ) + y1 ( d - cos Ө ) + T’( y )
THE REFLECTION

## Slide 26
THE REFLECTION
xx = 4.20 yy = 11.80
icpx = 4.22 icpy = 11.82
deg = 0.00 icpdeg = 0.00
R:
1.00 -0.00
0.00 1.00
xx = 4.20 yy = 11.80
icpx = 4.20 icpy = 11.80
deg = 0.00 icpdeg = 0.00
R:
0.00 1.00
1.00 -0.00
Solved!

## Slide 27
Main Program

## Slide 28
THE END
THANK YOU VERY MUCH!
